Fall 1993
SWRUNNING
FOR 532 LABS

     Ecosystem simulation exercises with FOREST-BGC (Running and
Coughlan 1988, Running and Gower 1991), using climate and data
files from Missoula, Montana and Jacksonville, Florida.

EXERCISE 0.1. Run MT-CLIM for two slopes, a north-facing 0deg
aspect, 30% slope, and a south-facing 180deg aspect, 30% slope and
compare incident radiation loads thru the season.

EXERCISE 1. Photosynthesis
     Run Missoula under standard conditions for 1 year. What % of
the annual PSN was fixed in the non-growing season (for this
defined as YD 0-90 + 270-365)? Calculate a simple water use
efficiency of PSN/TRAN, X[6]/X[3].
     Now 2X maximum mesophyll conductance B(16) to 0.0016, and
maximum leaf conductance B(11) to 0.0032, and rerun. How has non-
growing season PSN changed, and PSN/TRAN changed?
     Change PSN temperature curve from 0-40deg (B[17], B[18]) to -
5-25.
     Change light response curve, 432-9720, (B[14], B[15]) to 200-
5000 a highly tolerant tree, and 800-20,000 a highly intolerant
tree.

EXERCISE 2. Respiration
     Increase B[19],[20],[21] by 2X and compare final annual PSN to
standard run. Now run standard and 2x respiration run for 10 years
(STOP = 3650 days, .GRW output file ON, .DAY OFF) and compare
results of additional respiration loading. With the original values
for B[19,20,21] simulate a huge old growth tree with stem carbon
X[9] = 300E+3 for 1 year, look at the .DAY file and compare the
maintanence respiration costs to the original run.

EXERCISE 3. Carbon Budgets and Regional Productivity. Do a 20 year
simulation for Missoula, and Jacksonville, Florida (JAC84).
Calculate the fractions of leaf, stem, root growth, construction
and maintanence respiration by comparing against the Gross primary
production (GPP), in the .GRW file. Calculate a simple growth
efficiency of þStemC/LAI (Leaf area index, defined here as Leaf
C/Specific Leaf area, or X8/B1) for each at Year 10. Compare the
results from these contrasting climates.

EXERCISE 4. Tree water relations
     To illustrate the role of soil as a system water capacitance,
change B[3] from 2350 (23.5cm) down to 1000 (10cm), then up to
40cm. Run for 1 year for both Missoula as a cool, dry climate, and
Jacksonville as a hot wet climate.
      To look at the importance of stomatal physiology in tree
water balance, do one year runs changing individually,  maximum
leaf conductance B[11] from 0.0016 first down to 0.0005, then up to
0.005, what happens to seasonal water use? Next B[13], the humidity
reduction factor, change first from 0.05 to 0.01, then to 0.1.
Finally, change the leaf water potential at stomatal closure B[12],
from 2.0, first to 4.0, then to 1.2.

EXERCISE 5. Hydrology
     Do a 1 Year simulation with LAI = 3,6,9 by changing X[8] =
1.2, 2.4 and 3.6 E+3, for both Missoula and Jacksonville. Note the
change in PSN, ET and Outflow.
     Initiate model runs for Missoula with snowpack of 4.32cm, X[1]
= 432, now do 2432, or 24.32cm, equivalent to a high mountain site.
How much does PSN, ET and Outflow change?
     Change the canopy interception coefficient, B[4] from 0.0005,
first to 0.0, no canopy interception, then to 0.002; and evaluate
a 1 Year run for Missoula.

EXERCISE 6. Nutrient uptake, Nitrogen use efficiency
     Reduce B[39] and B[40], the nitrogen inputs from 5.0 kg/yr to
0.0, and run the model for 20 Years, for both Missoula and
Jacksonville. Then re-run with B[39] = 50kg/yr, a rate measured in
some Belgian forests. Compare to standard 20 Year runs of 5kg/yr.
Calculate a nitrogen use efficiency, as NPP/N from
þX[8]+X[9]+X[10]/G[52], at Year 20. We will use the .LNG files for
this.

EXERCISE 7. Leaf, Root turnover
     Change B[32] leaf turnover rate, 1/yr, from 4 yr to 1 yr, and
Specific Leaf area, B[1] from 25 to 75, effectively a deciduous
tree, and run Missoula for 20 Years. Remember to also change the
Leaf On-Leaf Off dates to 100-290 in B[36,37]. Then change B[32] to
10 years, simulating a true fir or spruce and re-run. Try all this
for Florida, and see if climate interacts with optimization of leaf
longevity.

EXERCISE 8. Decomposition
     Change the decomposition temperature rate control, B[46] from
50ø to 30, then to 70ø, and run Jacksonville for 20 years. Do the
same for Missoula, and compare the rates of decomposition (for the
50deg runs only) in the cold dry Montana climate relative to the
hot,wet Florida climate.

EXERCISE 9. Climate Change
     I will hand out a .CLM file for Missoula that represents a
best guess of a 2X CO2 climate, +4degree air temperatures and dew
point, and +10% precipitation. Run FOREST-BGC for 100 yrs with the
current climate file, then the climate change file, and look at the
difference in Stem carbon accumulation.