## Slide 1: InVEST (Integrated Valuation of Ecosystem Services and Trade-offs) Water Purification: Nutrient Retention
Host Institution/URL
  http://www.naturalcapitalproject.org
Objective
  Improve policies and planning by incorporating ecosystem nutrient retention capacity with land use
  Model scenarios for spatial planning and/or environmental impact assessments
Key Assumptions and limitations
  Hydrologic system not dominated by rainfall intensity events
  - Nutrient Transport is continuous
    i.e. Does not include diches that may speed up run-off into stream
  Riparian Vegetation the only factor considered for water purification
    i.e. does not represent biological/chemical processes for retention/degradation
  Assumes marginal cost for pollution treatment
Temporal/Spatial Scale
  Annual average, NOT an event based model
  local to regional watershed scale

## Slide 2
InVEST Inputs
Supply
DEM – Digital Elevation Model – data set with elevation for each cell
Water yield per cell- delineated by reservoir or interest pts.
Root restricting later (mm)
Precipitation (mm)
Plant available water fraction
Avg. Plant Evapotranspiration (mm)
Nutrient loading (kg/Ha/yr)
Nutrient filtration efficiency %
Threshold flow accumulation value-
# of cells nutrient is transported before waterway
Service
Time span (years of nutrient retention)
Value of pollution retention
Mean annual nutrient removal cost $/kg pollutant removed
Discount rate (%)
  InVEST Outputs
  Total exported nutrient (kg/ha/watershed):
  Total nutrient retained (kg/watershed):
  Nutrient Stream loading (kg/pixel)
  2 Maps
    Showing nutrient production, and
    load retention downstream (kg/pixel)
  Value of nutrient retained over time period (currency/time):
Water Retention Model

## Slide 3
Earth Observation for Ecosystem Valuation, EARSC
Lombok, Indonesia
InVEST:
Lessons from the Field and
Measuring success
http://www.hobgreeneconomy.org/en/invest
Research and Applications