## Slide 1: OTIS, One-Dimensional Transport with Inflow and Storage. http://water.usgs.gov/software/OTIS/ Developed by R. Runkel, USGS Presented by: Nicholas J. Banish, Valett Aquatic Ecosystems Ecology Laboratory, UMT DBS
Domain/Objective:
Characterizes the fate and transport of waterborne solutes in lotic systems. Used in conjunction with field data to quantify hydrologic processes and chemical transformations that affect solute transport
Framework for integrating different types of data (Q, Qsub, nutrient Uptake). Given a description of watershed loading, OTIS determines solute concentrations that result from hydrologic transport and chemical transformations.
HYDROLOGIC PROCECESSES CHEMICAL TRANSFORMATIONS
Advection Sorption
Dispersion First Order Decay
Transient Storage
Key Assumptions: 1-D Advective/Dispersive Transport of solute mass. [c] varies only longitudinally, (not w/ w or z) i.e., solute mass is evenly distributed over x-sect. area of stream. Conservation of Mass applies for both in-channel and T.S.Z. compartments.
Temporal/Spatial Scale: 1-D => Longitudinal. Can be Spatially expansive. Integrates across scales of surface-subsurface exchange
cumulative effects of chemical rxn’s and hydrologic storage on solute fate (though not necessarily process specific). Relatively large spatial scale.
Kaplan, L.A. et al. Untangling the complex issue of dissolved organic carbon uptake: A stable isotope approach: Freshwater Biology, v. 53, no. 5, p. 855-864, doi:10.1111/j.1365-2427.2007.01941.x
Valett, H.M., et al. 1996, Parent lithology, surface-groundwater exchange, and nitrate retention in headwater streams. Limnology and Oceanography, v. 41, no. 2, p. 333-345.
Tank, J.L et al. Are rivers just big streams? A pulse method to quantify nitrogen demand in a large river: Ecology, v. 89, no. 10, p. 2935-2945, doi:10.1890/07-1315.1

## Slide 2
Main Channel Assumptions:
physical processes
RXN’s affecting solute [c]
parameters describing physical processes and chemical reactions may be spatially variable.
parameters describing advection and lateral inflow may be temporally variable; include: Q, X-S area, QLIN, [c] assc. w/ QLIN. All other model parameters are temporally constant.
Storage Zone Assumptions
physical processes do not occur in S.Z. Transient storage is the only physical process affecting solute [c]
Chemical RXN’s affecting solute [c].
All model parameters describing transient storage and chemical reactions may be spatially variable.
All model parameters describing transient storage and chemical reactions are temporally constant.
Input Drivers:
Physical
Main channel x-sect area is used with estimates of streamflow to determine avrg. advective velocity of transported solutes
spreading of solute mass due to shear stress described by D, dispersion coefficient
Solute mixing due to T.S. governed by S.Z. x-sect. area and S.Z. coeff (α)
Lateral Inflow, and assc. [c] with Lin
Chemical: 2 types of Chemical RXN’s
First order decay; may be specified for main channel (and/or) S.Z.
Sorption: distribution coeff. based on chemical sorption onto streambed.
parameter file: sets simulation options, boundary conditions, and model parameters that remain constant throughout the run.
flow file: contains model parameters that
can potentially vary during the simulation (for example, volumetric flow rate and main channel cross sectional
area)
Key Outputs:
A general equation in the form:
C(x, t) = Hydrologic Transport + Chemical Transformations

## Slide 3: Model Validation – Examples of Results
Trial and Error: Bencala and Walters use Cl as conservative tracer to model Transient Storage, varied physical parameters to obtain match b/w observed and simulated results. Pool areas are large relative to main channel
Parameter Estimation: Laenen and Risley used Nonlinear Regression for parameter estimation; travel times (A) mixing characterisitcs (As, α, D) can be determined
Nutrient Uptake:
McKnight and Duff estimate nitrate uptake by algal mats in main channel and T.S.Z. in Antartica. Based on observed concentrations, inferred loss of 84-93% of NO3 in main channel by geochemical processes
Trace Metal Removal:
Used to determine steady-state solute concentrations that result from constant loading (dissolved Fe). Close fit b/w obs. and simulated conc. Suggest initial increase in Fe is due to strictly hydrologic factors. Decr. @ 500m do not match observed decr., indicating chemical rxn’s affect dissolved [Fe]